Bionet Demo Verification Procedure

# Objective
This plan documents testing of Bionet software and hardware for ensuring demonstration readiness. This document describes the verification at the highest level. Each device needs to be tested for its own correctness.
# Test Subjects
Bionet demonstrations require both software and hardware. These need to be tested in a stand-alone fashion and an integrated fashion.
## Software Testing
Bionet v2.1.2 and later has unit tests and integration tests built-in. The first measure of software verification is to compile Bionet and run the unit tests. The command 'make check' runs the unit tests. Next is to run the integration tests. The command 'make test' runs the integration tests.
# cd bionet
# ./configure
# make
# make check
# make test
Provided these steps all succeed without errors, Bionet has been shown to be operating correctly.
## Hardware Testing
The hardware needs to correctly interoperate with the Bionet Hardware Abstractors (HABs). In order to verify this the hardware to be tested needs to be present. All wired devices need to be plugged into the computer running the Bionet HAB software. Bionet Monitor can be used for all HABs. All wireless interfaces required need to be enabled and properly configured. The procedure for each Device/HAB is as follows:
- start Bionet Monitor
- start the HAB to be tested
- turn on or plug in the device to be tested
- ensure the device has been properly displayed as a node in Bionet Monitor with the correct resources and/or streams.
- ensure resource values are sane
See section 3 for HAB resource checklists.
# Hardware Abstractors
## Alsa HAB
√	Resource Name
	Microphone
	Speaker

## CPOD
√	Resource Name
	ECG-II
	Accel-X
	Accel-Y
	Accel-Z
	Temperature
	Pulse-Oximetry
	Heart-Rate

## CSA-CP
√	Resource Name
	O2

## MMOD
√	Resource Name
	Voltage
	RawVoltage
	Temperature
	RawTemperature
	Photo
	RawPhoto
	Accel-X
	RawAccel-X
	Accel-Y
	RawAccel-Y
	SampleInterval
	NumAccelSamples
	AccelSampleInterval
	HeartbeatTime
	AccelAxis
	MsgCounter
	MissedMsgs

## PAL-650
√	Resource Name
	X
	Y
	Z

## PARSEC
√	Resource Name
	Range
	Temperature

## Speedway
√	Resource Name
	Antenna-1
	Antenna-1-PeakRSSI
	Antenna-2
	Antenna-2-PeakRSSI
	Antenna-3
	Antenna-3-PeakRSSI
	Antenna-4
	Antenna-4-PeakRSSI
	GPI1
	GPI2
	GPI3
	GPI4

## Stethoscope
√	Resource Name
	Battery-Voltage
	Gain

## UWB
√	Resource Name
	X
	Y